## Slide 1: Observing CMEs with Solar Orbiter
D. Berghmans, C. Verbeeck (ROB)
SOLAR ORBITER SOWG #8 - ESAC, 25-28 JANUARY 2016
Notes: Disclaimer: this presentation is remote-sensing-centric. Apologies for that.

## Slide 2: Objective 2: How do solar transients drive heliospheric variability?
2.1 How do CMEs evolve through the corona and inner heliosphere?
2.2 How do CMEs contribute to the global evolution of magnetic flux in the heliosphere?
2.3 How and where do shocks form in the corona and in the heliosphere?
Notes: https://issues.cosmos.esa.int/solarorbiterwiki/pages/viewpage.action?pageId=9044404 show also all the subobjectives
The goal is to arrive at campaigns that address these objectives. How do we do that? -> next slide

## Slide 3: 2 approaches to identify optimal joint instrument operations
Given the state of the art on CMEs, what open questions remain to be answered by Solar Orbiter and how does this lead to optimal operations for Solar Orbiter instruments?
Given the Solar Orbiter constraints, what is the most sensible way to operate its instruments for CME observations?
Notes: Number 1 is what Russ presented just before.
Number 2 is what we will try here.
Note we do not want (and cannot) go into much details of the operations of each instrument. We merely try to identify group-strategies for the instruments to work together.
We also do not discuss individual instrument campaigns. Eg Solo HI might have a CME campaign independent of all other instrument, this is not discussed here.
So what are these constraints that will drive the instrument operations -> next slide

## Slide 4: Solar Orbiter constraints
Remote Sensing Window?
REMOTE SENSING INSTRUMENTS
ARE NOT ALWAYS ON
Off-pointing?
OFF-POINTING IS NOT
GOOD FOR METIS
Synoptic or triggered?
NOT ENOUGH TELEMETRY TO GO
FULL POWER ALL OF THE TIME
Notes: Like every mission, Solar Orbiter comes with constraints on the instrument operations (red).
The way we deal with these constraints, i.e. the choices we make (blue diamonds) will lead to different campaign strategies.
Obviously there are more constraints….
METIS is given a particular status, which is fair for a CME centered discussion

## Slide 5
START
Remote Sensing Window?
Off-pointing?
YES
1 . In-situ only campaigns
NO
+ TBD external support: Solar Probe Plus, STEREO, Earth-bound (LASCO, PROBA-3, SDO, ground-based, etc.)
NO HENCE
METIS ON
Synoptic or triggered?
2. High res
campaigns
YES, THUS
METIS OFF
3. Triggered campaigns incl. METIS
TRIGGER
4. synoptic campaigns incl. METIS
SYNOPTIC
Notes: Note that high-res catching of CMEs is only possible using triggers (otherwise statistics are _very_ unfavorable).
LASCO is predicted to run out of power by 2022!

## Slide 6: Type 1 campaigns, in-situ only
Out-of-RSW synoptic images still desirable
Scheduling for precise constellation with Earth or other spacecraft is important (cause/effect)
(we are not specialist on this)
Not treated further in this presentation
1 . In-situ only campaigns

## Slide 7
METIS is off
Short campaigns
Triggers needed to catch events
Scheduling is critical
Useful for high resolution
Preferentially at perihelion
High data production rate
Offpointing is possible
2. High res
campaigns

## Slide 8
METIS is on
Offpointing is not possible
Full disc remote sensing is primary, high resolution is secondary
Position in orbit is not critical
Moderate data production rate
Long campaigns
Scheduling is less critical
Triggers optional
4. synoptic campaigns incl. METIS
3. Triggered campaigns incl. METIS

## Slide 9
METIS off
Off-pointing possible
Focus on high resolution
Perihelion preferred
High data rate
Triggers needed to catch events
Short campaign
METIS on
Off-pointing constrained
Focus on full disc, but some hi-res possible
Phase in orbit not critical
Medium data rate
Event-hunting with triggers
Short/medium campaign
METIS led SOOP “CME-watch”
was exercised during SOWG-5
“Trigger Exercise”
during SOWG-6
3. Triggered campaigns
incl METIS
2. high-res
campaigns without METIS
METIS on
Off-pointing constrained
Mainly full disc
Phase in orbit not critical
Low data rate
No triggers
Long & slow campaign
4. Synoptic campaigns
Incl METIS
Not exercised yet?
Not exercised yet?
Notes: Constrained means that the pointing should allow METIS to be safely on. This does not necessarily mean pointing to disc center, especially when far from perihelion.

## Slide 10
METIS off
Off-pointing possible
Focus on high resolution
Perihelion preferred
High data rate
Triggers needed to catch events
Short campaign
METIS on
Off-pointing constrained
Focus on full disc, but some hi-res possible
Phase in orbit not critical
Medium data rate
Event-hunting with triggers
Short/medium campaign
METIS led SOOP “CME-watch”
was exercised during SOWG-5
“Trigger Exercise”
during SOWG-6
3. Triggered campaigns
incl METIS
2. high-res
campaigns without METIS
METIS on
Off-pointing constrained
Mainly full disc
Phase in orbit not critical
Low data rate
No triggers
Long & slow campaign
4. Synoptic campaigns
Incl METIS
Not exercised yet?
Not exercised yet?
Notes: Constrained means that the pointing should allow METIS to be safely on. This does not necessarily mean pointing to disc center, especially when far from perihelion.

## Slide 11
METIS off
Off-pointing possible
Focus on high resolution
Perihelion preferred
High data rate
Triggers needed to catch events
Short campaign
METIS on
Off-pointing constrained
Focus on full disc, but some hi-res possible
Phase in orbit not critical
Medium data rate
Event-hunting with triggers
Short/medium campaign
METIS led SOOP “CME-watch”
was exercised during SOWG-5
“Trigger Exercise”
during SOWG-6
3. Triggered campaigns
incl METIS
2. high-res
campaigns without METIS
METIS on
Off-pointing constrained
Mainly full disc
Phase in orbit not critical
Low data rate
No triggers
Long & slow campaign
4. Synoptic campaigns
Incl METIS
Not exercised yet?
Notes: Constrained means that the pointing should allow METIS to be safely on. This does not necessarily mean pointing to disc center, especially when far from perihelion.

## Slide 12
METIS off
Off-pointing possible
Focus on high resolution
Perihelion preferred
High data rate
Triggers needed to catch events
Short campaign
METIS on
Off-pointing constrained
Focus on full disc, but some hi-res possible
Phase in orbit not critical
Medium data rate
Event-hunting with triggers
Short/medium campaign
METIS led SOOP “CME-watch”
was exercised during SOWG-5
“Trigger Exercise”
during SOWG-6
3. Triggered campaigns
incl METIS
2. high-res
campaigns without METIS
METIS on
Off-pointing constrained
Mainly full disc
Phase in orbit not critical
Low data rate
No triggers
Long & slow campaign
4. Synoptic campaigns
Incl METIS
Not exercised yet?
Notes: Constrained means that the pointing should allow METIS to be safely on. This does not necessarily mean pointing to disc center, especially when far from perihelion.

## Slide 13
METIS off
Off-pointing possible
Focus on high resolution
Perihelion preferred
High data rate
Triggers needed to catch events
Short campaign
METIS on
Off-pointing constrained
Focus on full disc, but some hi-res possible
Phase in orbit not critical
Medium data rate
Event-hunting with triggers
Short/medium campaign
METIS led SOOP “CME-watch”
was exercised during SOWG-5
“Trigger Exercise”
during SOWG-6
3. Triggered campaigns
incl METIS
2. high-res
campaigns without METIS
METIS on
Off-pointing constrained
Mainly full disc
Phase in orbit not critical
Low data rate
No triggers
Long & slow campaign
4. Synoptic campaigns
Incl METIS
Not exercised yet?
Notes: Constrained means that the pointing should allow METIS to be safely on. This does not necessarily mean pointing to disc center, especially when far from perihelion.

## Slide 14
METIS off
Off-pointing possible
Focus on high resolution
Perihelion preferred
High data rate
Triggers needed to catch events
Short campaign
METIS on
Off-pointing constrained
Focus on full disc, but some hi-res possible
Phase in orbit not critical
Medium data rate
Event-hunting with triggers
Short/medium campaign
METIS led SOOP “CME-watch”
was exercised during SOWG-5
“Trigger Exercise”
during SOWG-6
3. Triggered campaigns
incl METIS
2. high-res
campaigns without METIS
METIS on
Off-pointing constrained
Mainly full disc
Phase in orbit not critical
Low data rate
No triggers
Long & slow campaign
4. Synoptic campaigns
Incl METIS
Not exercised yet?
Notes: Constrained means that the pointing should allow METIS to be safely on. This does not necessarily mean pointing to disc center, especially when far from perihelion.

## Slide 15
METIS off
Off-pointing possible
Focus on high resolution
Perihelion preferred
High data rate
Triggers needed to catch events
Short campaign
METIS on
Off-pointing constrained
Focus on full disc, but some hi-res possible
Phase in orbit not critical
Medium data rate
Event-hunting with triggers
Short/medium campaign
METIS led SOOP “CME-watch”
was exercised during SOWG-5
“Trigger Exercise”
during SOWG-6
3. Triggered campaigns
incl METIS
2. high-res
campaigns without METIS
METIS on
Off-pointing constrained
Mainly full disc
Phase in orbit not critical
Low data rate
No triggers
Long & slow campaign
4. Synoptic campaigns
Incl METIS
Not exercised yet?
Notes: Constrained means that the pointing should allow METIS to be safely on. This does not necessarily mean pointing to disc center, especially when far from perihelion.

## Slide 16
METIS off
Off-pointing possible
Focus on high resolution
Perihelion preferred
High data rate
Triggers needed to catch events
Short campaign
METIS on
Off-pointing constrained
Focus on full disc, but some hi-res possible
Phase in orbit not critical
Medium data rate
Event-hunting with triggers
Short/medium campaign
METIS led SOOP “CME-watch”
was exercised during SOWG-5
“Trigger Exercise”
during SOWG-6
3. Triggered campaigns
incl METIS
2. high-res
campaigns without METIS
METIS on
Off-pointing constrained
Mainly full disc
Phase in orbit not critical
Low data rate
No triggers
Long & slow campaign
4. Synoptic campaigns
Incl METIS
Not exercised yet?
Notes: Constrained means that the pointing should allow METIS to be safely on. This does not necessarily mean pointing to disc center, especially when far from perihelion.

## Slide 17
METIS off
Off-pointing possible
Focus on high resolution
Perihelion preferred
High data rate
Triggers needed to catch events
Short campaign
METIS on
Off-pointing constrained
Focus on full disc, but some hi-res possible
Phase in orbit not critical
Medium data rate
Event-hunting with triggers
Short/medium campaign
METIS led SOOP “CME-watch”
was exercised during SOWG-5
“Trigger Exercise”
during SOWG-6
3. Triggered campaigns
incl METIS
2. high-res
campaigns without METIS
METIS on
Off-pointing constrained
Mainly full disc
Phase in orbit not critical
Low data rate
No triggers
Long & slow campaign
4. Synoptic campaigns
Incl METIS
Not exercised yet?
Discussed at RSWG during SOWG-8
Notes: Constrained means that the pointing should allow METIS to be safely on. This does not necessarily mean pointing to disc center, especially when far from perihelion.

## Slide 18: Discussion
Full disc images throughout a long period (<= 1 RSW)
Catching coronal waves, halo CMEs that can be linked with in-situ signatures
This kind of campaigns can be run regularly (low telemetry cost)
“Simple is good” campaigns without trigger magic: risk free, scientific usefulness depending on CME-rate
4. Synoptic campaigns
Incl METIS
Notes: Long period is max 10 days, but eg 1 week is also reasonable.
Should be done during CME-rich period.
The thing about halo CME has been advocated by METIS people (Ester) before.
To be calculated what the cadence for each instrument should be.
This campaign could eg be useful to identify the source region of stealth CMEs, possibly high in the corona where FSI and METIS overlap.
If Solar Orbiter and Earth see the event at different angles, we get 3D information.
If you don’t catch a CME you will still have a nice global view of the inner heliosphere and its evolution over 10 days
PHI: 5-10 min cadence Full Disk vector magnetograms & LOS velocity. Stores all data internally; selection a-posteriori from ground
SoloHI: Observing over East limb (as seen from SO): ~30-min full FOV (40 deg) and TBD hrs of 6-min partial FOV (ecliptic 5x40 deg)
SPICE: “CME watch”: 5 line profiles, 10 intensities; 4’’ slit, 30 s exp; X=90 times ; 30 repeats gives 22.66 h duration.

## Slide 19: Discussion
Similar to previous case but with triggers
EUI can either:
  Run high cadence FSI/HRI images and freeze buffer when EUI/METIS/STIX trigger fires
  Run medium cadence, store all data internally; selection a-posteriori from ground
METIS & STIX trigger on. @METIS trigger: METIS cadence 15 min -> 1 min
SoloHI: medium cadence, high res images
quadrature/alignment with SPP, STEREO, Earth?
Possibility to catch good event in high/medium cadence but more complexity
3. Triggered campaigns
incl METIS
Notes: Should be done during CME-rich period.
To be calculated what the cadence for each instrument should be.
This campaign could eg be useful to identify the source region of stealth CMEs, possibly high in the corona where FSI and METIS overlap.
If Solar Orbiter and Earth see the event at different angles, we get 3D information.
After the SOWG-5 exercise we all felt this looked feasible.
SoloHI: 30-min synoptic FOV + TBD hrs 6-min 5x40 deg FOV
SPICE: “CME watch”: 5 line profiles, 10 intensities; 4’’ slit, 30 s exp; X=90 times ; 30 repeats gives 22.66 h duration.
SoloHI: Observing over East limb (as seen from SO): ~30-min full FOV (40 deg) and TBD hrs of 6-min partial FOV (ecliptic 5x40 deg)

## Slide 20: Discussion (I)
Decision to close METIS taken at LTP (T – 6 or 12 months). VSTP (T – 2 days): possibility to offpoint
Low event stats → trigger (EUI, STIX) is essential to catch eruption in high res FOV
High cadence, high res images over very short period (few hours) defined by trigger
@trigger:
  EUI freezes its 1-hour-buffer
  SPICE: high cadence, smaller slit
  SoloHI: high cadence, high res images
Superior cadence & res imaging of source region, flares, dimmings, EUV waves
2. high-res
campaigns without METIS
Notes: Note: HI can react on the fly as it takes some time before eruption arrives in HI field of view.
PHI: 5-10 min cadence high res vector magnetograms & LOS velocity. Stores all data internally; selection a-posteriori from ground
SoloHI: Observing over East limb (as seen from SO): ~30-min full FOV (40 deg) and TBD hrs of 6-min partial FOV (ecliptic 5x40 deg).
Triggering a special higher cadence (than 6 mins) in case of an M5 or larger flare on the East hemisphere, is still TBD
  SPICE: “Dynamics”: 4 profiles, 6 intensities; 2’’ slit, 5 s exposure; X=120 times; 10 rasters gives 1.71 h

## Slide 21: Discussion (II)
At perihelion. Extra geometric criteria: quadrature/alignment with SPP, STEREO, Earth?
Strategy TBI when multiple sequential triggers are produced…
Challenging concept → make sure to always get some useful data even if main objective is not achieved
Aimed at catching a major event in highest cadence and resolution. Complex.
2. high-res
campaigns without METIS
Notes: Offpointing: This is going to be a tough decision.

## Slide 22
2.1 How do CMEs evolve through the corona and inner heliosphere?
2.1.1 What are the global structure, initiation, and evolution of CMEs?
2.1.1.1 CME initiation: 2
2.1.1.2 CME structure: 3, 4
2.1.1.3 CME evolution: 3, 4
2.1.2 Type II radio bursts: 4
2.1.3 Determine field line lengths using energetic particle travel time measurements: in situ only
Obj. 2: campaigns versus
science goals

## Slide 23
2.2 How do CMEs contribute to solar magnetic flux and helicity balance?
2.2.1 How do CMEs contribute to the global evolution of magnetic flux in the heliosphere? 2, 3
2.2.2 What is the role of ICMEs in the Sun’s magnetic cycle? 3
2.2.3 Determine connection/disconnection by identifying SEP dropouts and tracking field line: 3
Obj. 2: campaigns versus
science goals

## Slide 24
2.3 How and where do shocks form in the corona and in the heliosphere?
2.3.1 Coronal shocks: 4
2.3.2 What are the properties and distribution of heliospheric shocks?
2.3.2.1 Understand coronal conditions under which the shocks form and determine the interplanetary conditions where they evolve: 4
2.3.2.2 Identify interplanetary shocks and characterise their spatial and temporal evolution: in situ + SoloHI
2.3.2.3 Study heating and dissipation mechanisms at shocks with radial distance: in situ + SoloHI
2.3.2.4 Identify mechanisms that heat the thermal solar wind particle populations near shocks and determine their energy partition: in situ + SoloHI
2.3.2.5 Correlate coronal shocks passage with in situ measurements: 4
Obj. 2: campaigns versus
science goals
Notes: SoloHI in shock and synoptic modes according to SAP. Does this fall within what they would do in the four campaign types we’ve considered?

## Slide 25
2.3.3 Resolve the interplanetary shock field and plasma structure down to the spatial and temporal scales comparable and smaller than the typical ion scales: in situ only
2.3.4 Shock-surfing acceleration mechanism: in situ only
2.3.5 Understand the radio emissions from the ICME driven shocks: 4
2.3.6 Identify shock accelerated particles: 4
Obj. 2: campaigns versus
science goals
RS contributions to all science goals probably covered by 3 campaign strategies
Notes: Probably: not entirely clear whether the SoloHI part of the in situ + SoloHI objectives can be done with these 3 campaign strategies

## Slide 26
START
Remote Sensing Window?
Off-pointing?
YES
1 . In-situ only campaigns
NO
+ TBD external support: Solar Probe Plus, STEREO, Earth-bound (LASCO, PROBA-3, SDO, ground-based, etc.)
NO HENCE
METIS ON
Synoptic or triggered?
2. High res
campaigns
YES, THUS
METIS OFF
3. Triggered campaigns incl. METIS
TRIGGER
4. synoptic campaigns incl. METIS
SYNOPTIC
Notes: Just back to grand overview.

## Slide 27: Conclusion
Obvious Solar Orbiter constraints lead to different sorts of campaign strategies
Within each particular campaign, details are to be discussed/filled in
All remote sensing contributions to Objective 2 are probably covered by 3 campaign strategies