## Slide 1
Commission 4 - Positioning and Applications
SC 4.3: Atmosphere Remote Sensing
Overview of CVC IAG WG 4.3.9
Monitoring ash-laden plumes using geodetic remote sensing techniques
Hugues Brenot1,*, Riccardo Biondi2, Flavio Cannavò3, Mohammed Hammouti6 , Samuel Nahmani4, Eric Pottiaux5, Rohm Witold7
http://iag.tomography.igig.upwr.edu.pl
Session 3.12: Dynamics of volcanic eruption plumes: models and observations
* Contact Author: brenot@aeronomie.be
Convective cloud using ground-based GNSS
Volcanic plume using ground-based-GNSS
Frame work
IAG WG 4.3.9 Observing convective and volcanic clouds
(1) (2) (3) (4) (5) (6) (7)
https://geodesy.science/com4
IUGG
Commission 4 – Positioning and Applications 2023-2027
Sub-commission 4 3 – Atmosphere remote sensing
WG 4.3.9 Observing convective and volcanic clouds with geodetic remote sensing techniques
Nowadays, the ground-based and space-borne geodetic observation techniques — including GNSS, satellite altimetry, VLBI, SLR, DORIS, and radio occultations — provide valuable information about the state and dynamic of the atmosphere.
Focus on advancing positioning, navigation, and timing (PNT) technologies, with an emphasis on GNSS and alternative systems. It aims to improve positioning integrity, sensor integration, and geodetic applications, addressing challenges such as interference and atmospheric disturbances.
Sensing ionosphere & neutral atmosphere
Motivation: Convective and volcanic clouds (CVC) represent a risk for population aviation safety which requires:
  improved CVC detection using GNSS (GB & RO);
  a better characterisation of the hazardous source (composition, cloud height, thickness, and density).
GNSS radio-occultation (RO)
Ground-based GNSS (GB)
GNSS analysis:
  GNSS RO: generating anomaly detection with respect to reference data
  GNSS tomography to retrieve 3D-structure (slant delay analysis with ZTD, gradients and residuals
  Develop diagnostic tool from slant delays observations (delays disturbance and SNR).
Flash-flood (8-9th September 2002)
Pont du Gard in October 2007.
Extreme event (25 dead mans, 691 mm of precipitations in 24h)
Mt Etna 2018 eruption
Temperature anomaly (K) Temperature anomaly (K)
Etna activities on 24 (a) and 27 (b) December 2018 as seen from Enna and Taormina (credits Truscia L. and Ponzo C.). Image from Corradini et al. (2019, IGARSS)
ZTD & gradients every 5 min Daily calculation using GipsyX latest version (2.3)
GPT2 mapping function; cut-off angle of 10°
ZWD constrained to follow a random walk of 5 mm/√h
Tropospheric gradient constrained to 0.5 mm/√h
Reading station metadata from the RINEX file header
Using JPL products by default for PPP processing with GipsyX's gd2e script
No 2nd-order ionospheric correction
cut-off 10°
cut-off 30°
ECOR
ECRI
EBAG
cut-off 10°
cut-off 30°
Ice particles is observed by SEVIRI in the ash-laden plume using RGB cobra composite.
For COBRA algorithm on SO2 / ash / ice see Poster Board Number: 72
Presentation time: Friday 16:30 - 18:00, Room Poster Hall
Link to animation
G7
Consequent quantity of water vapour (wet delays) in the boundary layer above EBAG station (280 m asl.) in comparison to ECOR (1240 m asl.) and ECRI (1480 m asl.). Can this be only the results low layer flux of water vapour combined with the orographic effects?
One way post-fit residuals shows higher values for ECRI and ECOR stations
 impact on low elevation signal
How can the East gradient between the ECRI and ECOR stations (only 500 m apart) be so different?
C1 Pseudorange on L1 (C/A code) Code-based range using civilian signal on L1 (1575.42 MHz).
P2 Pseudorange on L2 (P(Y)-code) Code-based range using encrypted P-code on L2.
D1 Doppler on L1 Doppler shift of the L1 carrier; used to estimate relative velocity.
D2 Doppler on L2 Doppler shift of the L2 carrier (1227.60 MHz).
S1 Signal-to-noise ratio on L1 SNR on L1 signal, typically in dB-Hz.
S2 Signal-to-noise ratio on L2 SNR on L2 signal.
Action plan:
  Setting benchmarks campaigns and synergy of GNSS analysis with:
  - other remote sensing techniques (GEO imagers and LEO sensors for plume geo-location, gas composition and structure of the volcanic plume)
  - ground-deformation and seismicity for understanding the mechanisms of an eruption.
Brenot, H. (2020). GNSS for Neutral Atmosphere and Severe Weather Monitoring. In Position, Navigation, and Timing Technologies in the 21st Century (eds Y.T.J. Morton, F. Diggelen, J.J. Spilker, B.W. Parkinson, S. Lo and G. Gao). https://doi.org/10.1002/9781119458449.ch30
Biondi, R., Steiner, A. K., Kirchengast, G., Brenot, H., and Rieckh, T.: Supporting the detection and monitoring of volcanic clouds: A promising new application of Global Navigation Satellite System radio occultation, Advances in Space Research, Volume 60, Issue 12, 2017, p. 2707-2722, ISSN 0273-1177, https://doi.org/10.1016/j.asr.2017.06.039.
Volcanic plume using GNSS radio-occultation
Liquid and solid water (hydrometeors) can disturb GNSS signal and induce delays of propagation.
Flash-flood Gard 2002
Nabro June 2011 eruption